## Slide 1
FPGA BASED IMAGE PROCESSING WITH SOBEL FILTER
Team 1 : Sl24225001 - Sl24225007 - Sl24225008

## Slide 2
  Introduction
  Background and Motivation
  Methodology and implementation
  Result
  Conclusion
OVERVIEW

## Slide 3
  Image preprocessing is a crucial first step in computer vision workflows.
  Enhances input image quality by reducing noise and highlighting features.
  This project focuses on implementing the Sobel edge detection algorithm on an FPGA to accelerate preprocessing.
  Target hardware: Xilinx ZedBoard using the MNIST dataset
INTRODUCTION

## Slide 4
FPGA is a reconfigurable hardware device. Unlike CPUs or GPUs, where the architecture is fixed, an FPGA can be custom-wired to perform specific tasks.
BACKGROUND AND MOTIVATION

## Slide 5
Edge detection is a technique used in image processing to identify the boundaries of objects in an image. It works by detecting sharp changes in pixel intensity, which usually correspond to edges.
The Sobel filter is a widely used edge detection operator. It uses two 3×3 kernels (one for detecting horizontal edges and one for vertical edges)
BACKGROUND AND MOTIVATION

## Slide 6
Advantages of Using FPGA:
  Parallelism FPGAs can compute many pixels simultaneously.
  Low Latency :fast hardware logic response.
  Real-Time Processing :Great for video streams (e.g., cameras, drones).
  Custom Hardware Logic : You can optimize performance & area.
  Lower Power (vs GPU) : Ideal for embedded & battery-powered systems.
BACKGROUND AND MOTIVATION

## Slide 7
METHODOLOGY AND IMPLEMENTATION

## Slide 8
METHODOLOGY AND IMPLEMENTATION
  used python to apply sobel filter
  understant how sobel filter works
  have a vision of the result more easily

## Slide 9
METHODOLOGY AND IMPLEMENTATION
  Rewrote the Python logic in C++ using Vitis HLS.
  Optimization techniques:
    Loop pipelining
    Loop unrolling
    Bit-width reduction to fixed-point
    Array partitioning
  RTL exportation

## Slide 10
METHODOLOGY AND IMPLEMENTATION
  Vivado project targeted the ZedBoard
  Sobel IP core integrated with AXI interfaces. - PS7 (Processing System) configured for DDR, UART
  Interconnects established
  Bitstream generated after validation and synthesis

## Slide 11
METHODOLOGY AND IMPLEMENTATION

## Slide 12
Thank You
For your attention